## Slide 1: How IXPs are supporting the Internet during COVID-19
Kenneth Chan
HKIX
25 Jun 2020

## Slide 2: Coronavirus Disease (COVID-19) in Hong Kong
Chart: 
Total Cases: 1,178 Confirmed / 89 Hospitalized / 1 Critical / 6 Death (as of 23 Jun 2020)
First case confirmed on Jan 23
Government announced its office closed from Jan 29
All schools closed from Feb 3 to May 26 after Lunar New Year holidays
Government office started to resume on Mar 2
Government announced office resumed on May 5
Schools gradually resumed from May 27 and onwards
Government announced office closed again on Mar 22
Schools Closed
WFH
WFH
No. of new confirmed cases (Jan 23 - Jun 21)
Feb 3 The Education Bureau announced all schools closed. Universities and colleges were started moving to online teaching
Jan 29 All government employees were instructed to work from home. Some organization and companies followed the arrangement.
Mar 29 Indoor and outdoor gatherings were limited to 4 persons
Apr 1 Karaoke lounges, nightclubs and mah-jong premises closed
May 5 Some of above premises were reopening and the cap for gathering has increased to 8 persons
Jun 19 The cap for gathering was relaxing to 50 for outdoor and unlimited for indoor
Apr 3 Pubs and bars were ordered to close for 14 days
Feb 4 Reported first death in HK
Mar 25 Hong Kong closed its border to all incoming non-residents
Jan 25 HK government declared the viral outbreak as an "emergency"
Notes: https://en.wikipedia.org/wiki/COVID-19_pandemic_in_Hong_Kong

## Slide 3: HKIX Traffic – Before and after work from home
˜35% increases on peak traffic
Traffic patterns are similar (e.g. peak and non-peak time)
Traffic was increased faster in the morning between 0600 and 1200 (83Gbps/hr158Gbps/hr)
The duration of peak time was longer (2hrs3hrs)
~30% increases on daily average
After WFH: 4 Apr 2020
Yearly Graph (1-day Average)
Yearly Graph (1-day Average)
Daily Graph (5-minute Average)
Daily Graph (5-minute Average)
Before WFH: 3 Jan 2020
Peak duration
Peak duration
0600-0900
500Gbps
950Gbps
0600-0900
Jan 23

## Slide 4: Some observations on traffic and port demands during COVID-19
People are forced or recommended WFH during the COVID-19 outbreak
Number of ports increased (29% on 100GE and 3% on 1/10GE)
HKIX traffic increased ˜35%, from 1.3Tbps to ~1.75Tbps from late Jan to mid Apr
The increased traffic was mainly from various online platforms
  Video conferencing / collaboration tools
  Online teaching / e-learning
  Video streaming
  Online gaming
  Internet banking
  Online shopping
Most of these providers had 30-40% traffic increment while video conferencing, Internet banking and online shopping had a record of 200%-300% significant growth

## Slide 5: Impacts on IXP operations at HKIX
  All sales orders are being handled and processed by emails
  Technical support and provision team could work from home to provide the services
  Pre-installed cabling infrastructure and switch ports at HKIX to speed up the provision of service
  Local loop providers to install the circuits and perform onsite testing
  Remote NOC to provide 24/7 non-stop operational services
  Network maintenance and project works were postponed

## Slide 6: Additional services and support for customers
  Precaution measures against COVID-19 in Data Centre
  NOC to provide 24/7 network monitoring and support services
    Monitor traffic usage on inter-switch links and participant links
    Reminder emails were sent to participants when the links are full
  Additional switches and inter-switch links deployment
    Additional switches are installed in core and satellite site
    Inter-switch links and inter-site links are added
  Allow customer suspend the service (max. 3 months) temporarily to reduce the cost upon request

## Slide 7: Thank You! For enquiries, please contact us at info@hkix.net